## Slide 1: InfraWorks KFT
Final Exam Project
Team Members:
Tóth Richárd (PM)
Schäfer Kristóf,
Date: 2026

## Slide 2: The Project Vision
Architecture: Three-tier (Core, Distribution, Access) hierarchy.
Redundancy: Dual ISP, redundant firewalls and Core switches.
Segmentation: Floor-by-floor separation and dedicated DMZ for servers.
Technologies: HSRP for fault tolerance, LACP for bandwidth.

## Slide 3: A Projekt Layout Overview

## Slide 4: What's Included in the Topology

## Slide 5: 2. DMZ (Demilitarized Zone)
DMZ Network Summary
Function: Isolation of public servers from the internal network.
Device: Cisco 2960 (Dedicated DMZ-SW).
Network: 10.11.11.0/27 (Mask: 255.255.255.224).
Range: 10.11.11.1 – 10.11.11.30.
Servers:
WEB: Website (HTTP/S)
EMAIL: Mailing (SMTP/IMAP)
FTP: File Transfer (SFTP)
APP: Business Apps (API)
NAS-STORAGE: Central Storage (NFS/SMB)
Security: VLAN-based segmentation + Firewall restriction toward internal network.
Goal: Secure isolation of public services (WEB, EMAIL, FTP, APP, NAS) from the internal network.

## Slide 6: 3. The Network "Brain" – Core Network Redundancy and Control
Devices: 2x Cisco 3560 Multilayer Switch (CORE-SW1, CORE-SW2).
Applied Technologies:
LACP (EtherChannel): Bundling multiple links for high bandwidth.
HSRP: Virtual default gateway (Gateway) for continuous operation.
WLAN Controller (WLC): Central unit for all floor-level Wi-Fi access points.

## Slide 7: First Floor (Blue & Green Block) – Sales, HR and Logistics
Departments: Sales & Marketing, HR & Logistics.
Endpoint Devices:
Wired PCs and Laptops.
Network Printers (MK-PR, HR-PR).
Mobile Devices (Tablets, Smartphones).
Communication: IP phones at every desk (VoIP network).
Wi-Fi: Dedicated access points (Access Points).

## Slide 8: Departments: Finance & Accounting, Admin & Relations. Structure: Identical to the first floor matching structure (standardized deployment). Network: VLAN-based segmentation for data protection. Devices: Dedicated Access Switches (FIN-SW, ADM-SW) providing for uplink to the Core . .
2. Floor (Light Blue/Light Green

## Slide 9: IT Department (ICT): Operational oversight and development. Internal Network Services (Server-SW):   DHCP Server: Automatic IP address assignment to clients.   DNS Server: Internal and external name resolution.   RADIUS Server: User authentication and network security (AAA).
Third Floor and IT Hub (IT Department and Internal Servers)

## Slide 10
Management Network (Green Zone)
NET-SEC-PC (10.20.0.10): Central administrative workstation for network monitoring.
WLC-2504: Cisco Wireless LAN Controller corporate Wi-Fi network and APs.
2811 Voice Gateway: Cisco router for VoIP (VoIP) traffic and PBX services.
This zone provides isolated access, separate from the DMZ- and internal network, for configuring network infrastructure (WLAN, Voice, Security)

## Slide 11: External Connectivity and Internet (INTERNET/CLOUD)
Central Cloud: The network connects via 8.0.0.0/8 to connect to the outside world
USA-INTERNET-USER (8.0.0.10): Remote US client access.
CHINA-INTERNETUSER (8.0.0.20): Remote Chinese client access.
Connections: Central routers (e.g., via 20.20.20.0/30 and 30.30.30.0/30 subnets) handle routing between sites and the internet.

## Slide 12: The Core Network (The "Heart" of the Network)
The two main switch (CORE-SW1 and CORE-SW2) handle the heavy lifting.
HSRP (Redundancy): Like a spare tire. If one switch fails, the other immediately takes over, and employees won't even notice the outage.
LACP (Bonding): Multiple cables are bundled between switches for faster data throughput, and if one cable fails, alternate paths remain.

## Slide 13: We created network virtual machines using the Oracle VirtualBox application

## Slide 14: Virtual Machines Used
Windows Server 2019
System: Windows Server-based environment with a graphical interface.
Network Config: Static IP address for reliable connectivity.
Debian
System: Debian Linux-based server with a custom user account.
Network Config: Static IP address configured for reliable connectivity.

## Slide 15: Active Services:
Web Server: Apache installed with HTTP(unencrypted) and secure HTTPS (encrypted) protocol support.
File Sharing: Samba service configured for cross-platform data access.
Data Protection: Automated backup configured using cron scheduler.

## Slide 16: Windows Server 2019 Infrastructure
Installation: Administrator environment and IPv4 configuration.
Directory: Active Directory and DNS service installation.
DHCP: Automatic IP address assignment to clients.
Resources: Centralized file and printer sharing.
Security: Scheduled backup (Backup Schedule) configuration.

## Slide 17: Debian/Linux Server System Environment: Debian OS installed with a custom user account and NAT network integration. Network Basics: Static IPv4 address configuration for fixed and reliable service access. Web Service: Apache web server with HTTP and secure HTTPS protocol support. File Management: Samba service for seamless data exchange between Linux and Windows platforms. System Security: Automated data backup process using cron task scheduler.

## Slide 18: Network Virtual Machines in Action
windows
Debian

## Slide 19: GIT – Version Control
What is it? Software, that saves for files' different states.
What is it used for?:
Traceability: Every change and responsible party is logged.
Rollback (Rollback): In case of errors, at any time you can revert to a previous, working version.
Teamwork: Multiple people can work on the same for project without, overwriting each other's work.

## Slide 20: JIRA – Project Management and Issue Tracking
What is it? A task management and process tracking framework.
How did we use it?
Task Assignment: Scheduling work items (e.g., cabling, procurement, installation).
Issue Tickets (Tickets): Recording and managing problems that arise during implementation.
Status Tracking: Monitoring progress with "To Do", "In Progress" and "Done" columns.
Deadlines: Meeting milestones and delivery dates.

## Slide 21: Testing

## Slide 22
Thank You for Your Attention!